## Slide 1
DRAFT PROJECT REPORT
Egocentric Hand Motion To Robot Simulation
Turning repeated first-person hand videos plus IMU context into smoothed hand intent, averaged motion, and MuJoCo simulation targets.
Interpolated handouts
Five-finger simulation
Training dataset
Current state
Working prototype
not robot-ready yet
The simulation can show the averaged hand motion, now including wrist rotation, while exposing where sensing and modeling still fall short.

## Slide 2
STARTING INTUITION
The first bet was biological, then practical
Hand meshes
A full hand mesh should be more faithful than sparse points because real hands are surfaces with anatomical constraints, occlusions, and contact.
Left as future work: robust egocentric mesh recovery needs more compute and model tuning than was available for this stage.
21-point tracking
MediaPipe landmarks made the project tractable: enough structure to estimate fingers and palm orientation, light enough to iterate quickly.
Tradeoff: easier to run, harder to recover metric depth and impossible to fully solve occlusion.
Egocentric hand motion to robot simulation
02

## Slide 3
SYSTEM FLOW
What the pipeline does now
Video + IMU
MediaPipe points
AHRS filter
IK smoothing
Full-frame data
Average action
MuJoCo render
The important change is that interpolation happens before dataset construction, so the model sees a complete action timeline instead of only the frames where the detector succeeded.
Egocentric hand motion to robot simulation
03

## Slide 4
MISSING FRAMES
The hard part was not detection, it was continuity
7,124
observation rows
full-frame dataset
72
features
landmarks + root + flags
6
videos averaged
same action family
360
average frames
canonical timeline
Each source video still has hundreds of IK-filled frames. That is not hidden; the handout overlays label detected versus interpolated frames so the uncertainty remains visible.
Egocentric hand motion to robot simulation
04

## Slide 5
LATEST CORRECTION
Wrist rotation moved into the motion target
AHRS camera attitude
Palm delta from landmarks
Smoothed root quaternion
+
The first reliable palm orientation becomes a calibration reference. Later palm poses become relative wrist rotation, composed with IMU/AHRS orientation and smoothed as quaternions.
Egocentric hand motion to robot simulation
05

## Slide 6
SIMULATION ARTIFACT
Five-finger render before robot attachment
Why Sharpa Wave?
The available Unitree G1 assets expose wrist joints but not a true five-finger articulated hand. Sharpa Wave from MuJoCo Menagerie gives a five-finger proxy for validating hand motion before robot attachment.
Output: outputs/sharpa_fivefinger_average_motion.mp4
Egocentric hand motion to robot simulation
06

## Slide 7
BASELINE
Learning signal: useful, but not yet enough
Chart: 
| Wrist roll | Wrist pitch | Wrist yaw | Thumb | Index | Middle
MAE radians | 1.1793 | 0.8092 | 1.7618 | 0.168 | 0.187 | 0.1313
Interpretation
The ridge baseline is a sanity check, not the final policy. Once wrist orientation became real, the wrist errors grew, which points toward a temporal model rather than a linear one.
Next model: GRU, TCN, or small Transformer over smoothed observation windows.
Egocentric hand motion to robot simulation
07

## Slide 8
ROADMAP
Limitations are clear, which is progress
Still limited by
• Image-normalized depth, not metric 3D
• Occlusion in egocentric footage
• Simple baseline model
• Five-finger proxy, not Unitree embodiment
• Standing balance not solved
Next steps
• Store world landmarks and timestamps
• Calibrate camera/IMU to robot frame
• Train a temporal policy
• Add whole-body balance controller
• Revisit mesh-based hand recovery with more compute
The prototype now makes the intended motion visible, including uncertainty. That is the right staging point before asking a humanoid robot to imitate it.
Egocentric hand motion to robot simulation
08